## Slide 1
Philip Conrad
Xander Jordan
Myndert Papenhuyzen

## Slide 2: Overview
Fall’s Accomplishments
Spring’s Accomplishments
Attack Vectors
Future Work
Notes: Myndert

## Slide 3: Fall’s Accomplishments
Took hardware inventory
Got equipment for testing
Got intel hex dump off of PEB & Reader
Notes: Myndert
Inventory – Chips and datasheets
Equipment – PICKit 3 and Bus Pirate
Hex Dump – Talk about MPLABX

## Slide 4: Spring’s Accomplishments
PEB Memory Dump
  SPI & UART protocols
  Discovered one PEB was dead
  Bus Pirate / Signal Eavesdropping
iVotronic JTAG
  Machine’s circuitry is not conducive
    Missing connections
Notes: Philip
SPI/UART – Mention what they are
Dead PEB – Some pins weren’t putting out voltage
iVo – Wiring is too complicated and lack equipment to check for continuity

## Slide 5: Attack Vectors
PEB – Based Attacks
  Changing Votes
  Discarding Votes
iVotronic – Based Attacks
  Denial of Service
  Arbitrary Code Execution
Viral Infection
Notes: Xander
Changing votes – aware/unaware voter
Discarding votes – use of fleeing voter
Denial of service – bad flash card sends iVotronic into bootloop
Arbitrary code execution – buffer overflow on a stack, can set return address anywhere we want

## Slide 6: Attack Vectors – Viral Infection
Notes: Xander
ES&S environment forms one big loop
Unity Election Management System configures PEB, Flash, and PCMCIA cards
These are necessary in calibrating the voting equipment
If we can sneak in a bad flash card and PEB, it is possible to create a ‘Viral Infection’
Infect iVos through bad PEBs
Bad iVos create bad PEBs
Bad PEB returns to Unity, infecting Unity
All media created from Unity will now be bad, compromising the election

## Slide 7: Knowledge for Future Groups
PEB programming pin configuration
PICKit 3 wiring configuration
Programming environment
Steps for future groups to take
Notes: Phillip
IRDa protocol stack
Reverse Engineering protocol between PEB and iVo
Working with memory modules on the iVotronic